## Slide 1: SparkFun ESP8266 Thing and Microsoft Azure

## Slide 2: Whe We Are
Bret Stateham
Technical Evangelist
IoT, Hardware, Making, Azure, C#
Mary Baker
Community Evangelist
Phil Cherner
Software Development Engineer
MR/VR/AR, IoT, Cognitive Services, C#, Python, Java, TypeScript, JavaScript, Azure

## Slide 3: Grab the Content
http://aka.ms/azurething

## Slide 4: Sign up for Azure
Best option is the Free Trial: azure.com/free
  Requires a credit card for identification purposes only
  Credit card WILL NOT be billed unless you authorize it
If you have signed up for a free trial before:
  You can’t use the same email address to sign up again
  Use a private browser session (no old accounts, cookies, etc loaded)
  Sign up for a new free email address at outlook.com
  Use that new email to sign up for the free trial (azure.com/free)

## Slide 5: Install Pre-Reqs
Arduino IDE 1.8.x https://www.arduino.cc/en/Main/Software
Azure Storage Explorer https://azure.microsoft.com/en-us/features/storage-explorer/
Node.js 8.x http://nodejs.org
Git http://git-scm.com
Azure CLI 2.0 https://docs.microsoft.com/en-us/cli/azure/install-azure-cli
FTDI Driver https://learn.sparkfun.com/tutorials/how-to-install-ftdi-drivers

## Slide 6
AZURE
FIELD
Resource Group <name>group
App Service Plan <name>plan
IoT Hub <name>iot
Stream Analytics Job <name>job
Storage Account <name>storage
Storage Table
TemperatureRecords
Service Bus Namespace <name>ns
Event Hub
TemperatureAlerts
Web App <name>web
INPUT
OUTPUT
OUTPUT
QUERY
RECEIVE
SEND D2C
RECEIVE C2D
GET
SEND C2D
Workshop
Architecture

## Slide 7: aka.ms/microsoftdocs

## Slide 9: Do a demo!

## Slide 10
AZURE
INGENU
FIELD
Ingenu RPMA Access Point
Ingenu Intellect Platform - REST or AMQP
Resource Group <name>group
App Service Plan ingenuplan
Function App ingenufunctions
Storage Account ingenustorage
Function IntellectRest2IoTHubJs
IoT Hub ingenuhub
Stream Analytics Job ingenujob
SQL Server ingenusql
SQL Database
ingenudb
Service Bus Namespace ingenubus
Event Hub
ingenualerts
Web App ingenuweb
Power BI Embedded Collection ingenucollection
Power BI Embedded Workspace Dynamic GUID
Power BI Report Temperature Chart
Function EventHub2IntellectRestJS
UPLINK
BACKHAUL
GET
SEND
READ/WRITE
INPUT
OUTPUT
OUTPUT
QUERY
GET
QUERY
RENDER
RECEIVE
POST
DOWNLINK
RPMA to Azure
Architecture Diagram

## Slide 12: IoT Logo

## Slide 13: arduino

## Slide 14: Arduino 101

## Slide 15: Grove Base Shield

## Slide 16: Grove cable & SENSORS

## Slide 17: Grove cable & SENSORS

## Slide 18: INTEL NUC DE3815TYKE

## Slide 19: GALILEO BOARD

## Slide 20: Raspberry Pi 3 PNG
https://commons.wikimedia.org/wiki/File:Raspberry_Pi_3_illustration.svg

## Slide 21: RASPBERRY PI

## Slide 22: FEZ SPIDER MAIN BOARD

## Slide 23: Sparkfun weather shield

## Slide 24: FEZ HAT

## Slide 25: Device graphics from docs
Device with Filled Holes
Device with Through Holes
This is a version of the Device icon used in the “Extended IoT Scenarios” in docs. For example: https://docs.microsoft.com/en-us/azure/iot-hub/iot-hub-explorer-cloud-device-messaging

## Slide 26: Connect the dots azure icons
Microsoft Azure
Event Hubs
Stream Analytics
Storage blob
Storage table
SQL database
(
generic
)
Storage
(
Azure
)
Web App
Machine
Learning
GitHub code
Git repository
Service Bus
HDInsight

## Slide 27: cables

## Slide 28: More cables and adapters

## Slide 29: LEDs
Long Leg
Short Leg
Small Post
Big Post
Flat Edge
Vcc (+)
GND
Anode (+)
Cathode (-)
Most reliable identification method

## Slide 30: LEDs

## Slide 31: Current limiting resistors
Providing more current than an LED is rated for can destroy the LED. To prevent that, you should use a “Current Limiting” resistor.
To calculate the value of the resistor you need to know the supply voltage (Usually 5V on the Arduino Uno), and the LEDs rated Forward Voltage (the voltage drop across the LED) and Forward Current (the maximum current the LED can handle).
The Arduino Uno has a built in current limiting resistor on Pin 13. If you use Pin 13 to power your LED you can use it without a separate resistor.

## Slide 32: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 33: Potentiometer – variable resistor

## Slide 34: breadboards
Breadboards offer a great way to prototype circuits. The provide a number of “buses” for connecting both power and components.
Power buses run the entire horizontal length
Component buses give you easy ways to connect pins together

## Slide 37: Micro SD Cards
Font: Segoe UI Semibold